## Slide 1: I-SEM CRM Local Issues
Emerging Thinking
Dundalk, 9 November 2016

## Slide 2: Content
Introduction and Summary
Auction design framework
  Auction format
  Clearing Price
  Compensation
  Representing constraints
Other Issues
  Grid Code
  Local security of supply and market power

## Slide 3: Workshop Overview
  Overview
    Present SEMC ‘emerging thinking’ positions on key items of Consultation 3a (local issues)
    Opportunity for discussion and feedback
    Notes from today’s session will be taken
  Introduction and Summary
    Project and process overview
    Outline of issue
    Key themes from responses to consultation
    Summary of emerging thinking

## Slide 4: Project Overview

## Slide 5: Ongoing Process
Work continues on rules and systems
Auction Timings
State Aid process
  Further engagement with DG Comp and DG Ener
Local Issues Process
  Consultation Issued on 24th August
  Consultation closed on 22nd September
  Detailed RA and SEMC consideration
  Decision scheduled for November SEMC
  Publish 8th December

## Slide 6: Outline of Issue
Background:
  Single capacity and energy zone
  In near term there will likely be more existing de rating capacity on the system than will be procured through the auction
At least initially there are significant transmission constraints:
  E.g. North-South and Dublin
Risk plant required for security of supply reasons in certain locations could exit
Issue needs addressed via some mechanism

## Slide 7: Outline of Proposal
Outline of proposal
  Consider significant locational capacity constraints in CRM
  If constraint binds select unit(s) required to meet constraints on a pay as bid basis
Benefits include
  Solve via market mechanism (recognising need for regulatory scrutiny)
  Provides transparency and simplicity
In medium to long term
  Network investment
  Effective locational signals
  If persistent consider zonal review

## Slide 8: Summary - Responses
Inclusion of locational constraints – mixed response with some push back
  Concerns raised include:
    State Aid approval
    Distortion of energy market
Alternative proposals suggested
  e.g. ancillary services, focus on network investment
Highlight difficulty in differentiating capacity constraints from ancillary services constraints
  Some argue all constraints should be included
Auction format
  Option B (procure for location in addition to unconstrained merit order) most favoured of options presented

## Slide 9: Summary – Responses II
Capacity clearing price
  Option 1 highest priced bid in unconstrained merit order preferred (i.e. unconstrained price)
  (alternative would lead to lower clearing price)
Compensation for unsuccessful in-merit bidders
  Mixed response but support for Option 1: No compensation
  Some proposed an alternative of paying full clearing price as compensation
Grid Code – current 3 year notice period
  Legal and economic concerns raised
  Some proposals to align with T-1 auction flexibility, change to 3 months, others propose 1 year.

## Slide 10: Summary – Emerging Thinking
Include locational constraints in CRM?
  Yes – only for capacity
Grid Code notice period
  Recognise concerns raised
  SEMC will have appropriate regards to statutory duties and where no local security of supply issues, request for derogation would be sympathetically received but not purely a CRM issue
Auction Format and Winner Determination
  In long run: Option D (full combinatorial)
  As transition: Option B (required plant selected in addition to unconstrained)
    To apply for transitional auctions

## Slide 11: Summary – Emerging Thinking II
Clearing price of auction
  Option 1 – unconstrained clearing price
  Most economically robust but potentially higher cost impact (at least in short term)
Compensation for unsuccessful bidders
  None
  For transitional auction applies only to inflexible bidders given Option B auction format
Representation of constraints
  Nested capacity areas with capacity requirement specified in MW
Constraints in T-4 Auctions
  Build in to auction systems
  Consult further before introducing into a T-4 auction

## Slide 12: Summary – Emerging Thinking III
Additional market power controls on existing plant required for locational reasons?
  Consideration ongoing
Additional market power controls on new build capacity required for locational reasons?
  Yes – limit multi-year pay-as-bid ROs above unconstrained price
  Some residual issues still under consideration

## Slide 13: Content
Introduction and Summary
Auction design framework:
  Auction format
  Clearing price
  Compensation
  Representing constraints
Grid Code
Local security of supply and market power

## Slide 14: Auction format: LSS consultation options
limited combinatorial element for inflexibility
Identify “must not exit” units ex ante?
Yes
Option A -Take must not exit units out of auction. Run simple sealed bid auction for remaining units
No
Select units to meet locational constraint additionally, or displace unconstrained winners
Additional
Displace
Option B. Unconstrained run based on simple sealed bid auction format, with additional units selected to meet locational constraints
Approach to managing locational constraint?
Full optimisation
Heuristic
Option D. Full combinatorial auction, subject to locational and lumpiness constraints
Option C. Heuristic second step, to manage capacity delivery constraint
Option E. TSO system security analysis to identify must-not exit units after an initial unconstrained run
Simple ex ante rules
Ex-post TSO security analysis
How are locational constraints evaluated

## Slide 15: Responses – Auction Design
Listed below in order of number of responses:
  No options justified on economic or legal grounds
  Option B: Simple sealed bid + constraints
  Option E: Unconstrained run then TSOs identify must run units
  Hybrid B&E: unconstrained run then full system
  security assessment, all in-merit receive
  CRM RO
  Option C: Simple sealed bid with heuristic step
  Option C and D: reflecting move to enduring combinatorial auction

## Slide 16: Responses – Alternatives suggested
Transmission related:
Need for focus on network investment
Strengthen TLAFs
Connection Policy and GTUoS signals
Other
Allow unrestricted bidding in the Balancing Market
TSO bi-lateral agreements
Ancillary services/DS3 scalers
CRM hybrids:
Hybrid Option B & E – two respondents
  Run unconstrained auction
  TSOs assess system security – TSOs bi-lateral agreement(s)
  All in-merit receive CRM RO
Other proposal
  Run unconstrained CRM and all in-merit receive a RO
  Offer “Strategic Reserve” contract required for system security reasons to each plant unsuccessful in CRM auction
    Contract for audited fixed costs + normal profit
    Plant required to bid into energy market at price of Long Run Fixed Costs – clearing price of CRM auction
    Clawback 95% of additional profit that plant make in energy market

## Slide 17: Rationale for high level approach
Why incorporate constraints in T-1 auction
Will be transmission constraints in transitional years
Need to ensure lights stay on - too greater a transitional risk, if do not incorporate
Preference for a competitive market based solution where possible, not bi-lateral negotiation
Chosen solution is market based, with one-year pay-as-bid contracts as a fall-back, similar to short term strategic reserve
Focus only on capacity, separate solution for ancillary services
The CRM is designed to assure capacity adequacy
  greater transparency if procure capacity only
  Purer price signal
Practical reasons support limiting the number of constraints- Inclusion of ancillary services constraints in CRM could involve a much larger set of constraints
Interaction between capacity and ancillary services constraints can be complex
Cannot provide solutions for first transitional years, but in longer run we will seek to:
Optimise trade-off between transmission and capacity investment
Consider further generator locational signals

## Slide 18: Key principles for locational framework
Any locational constraints taken into account within the CRM mechanism would only be used to represent local capacity deliverability constraints.
A locational need would only be included in the CRM mechanism where the need is clear and large.
The means by which local capacity deliverability constraints are identified and quantified would be simple and transparent to the maximum extent practicable

## Slide 19: Evaluation of Options
 | Key Pros | Key Cons
Option A: Ex-ante identification of “must not exit” units | Easy auction system to deliver In short run, lower customer bills than B, C, E. Possibly lower than D | Weak on competition where need X from Y in constrained area Lacks transparency Price set by plant outside NI and Dublin only Complicates State Aid?
Option B. Simple sealed bid auction format, with additional units for locational capacity | Strong on long run security of supply Easy auction system to deliver Potentially lower energy market revenues Longer term CRM benefits if prevents exit of plant cost effective once constraints alleviated | Higher CRM bills, at least in short term
Option C: Simple sealed bid, heuristic second step, to manage locational constraint | Lower CRM bills than B More competition and transparency than A, E TSOs say they can deliver for first auction | Higher energy market revenues Harder systems solution to deliver than A,B,E Weaker on security of supply than A,B, E? May increase concentration in energy market
Option D. Full combinatorial | Most efficient winner determination, long run Lower CRM bills than B, C, E | TSOs say they cannot deliver for first auction Weaker on security of supply than A,B, E?
Option E: Ex-post identification of “must not exit” units | Strongest on security of supply (TSO preferred): deals with unanticipated outcomes Stronger on competition than A Easy auction system to deliver | Weak on transparency, including CRM/ancillary service distinction Complicates State Aid?

## Slide 20: Content
Introduction and Summary
Auction design framework:
  Auction format
  Clearing price
  Compensation
  Representing constraints
Grid Code
Local security of supply and market power

## Slide 21: Locational constraints example
MW
€/kW
Highest accepted in-merit bid
Unconstrained price
All-island demand curve
€40
1
2
3
4
5
6
7
8
9
€35
Rejected for lumpiness (inflexibility)
Option 1: The highest-priced bid in-merit in the unconstrained merit order (€40).
Option 2: The highest-priced bid which is both: (a) accepted in the unconstrained merit order; and (b) selected as a winning bid after lumpiness consideration (€35)
NB: Location not relevant under Option B.

## Slide 22: Clearing price determination
Stakeholder response: Strong support for Option 1: Highest priced bid accepted in unconstrained merit order
Difference less material if no chance of multiple marginal /infra-marginal units rejected for locational reasons
 | Key Pros | Key Cons
Option 1 | Capacity price better approximation to the LRMC of capacity, so more efficient investment price signal Strong incentives for truthful bidding for most bidders | Higher customer bills Some gaming opportunities for bidders who are “constrained-off”, but think that they may set the unconstrained market price
Option 2 | Lower customer bills Gaming opportunities for bidders who are infra-marginal in unconstrained run | Price downward biased

## Slide 23: Content
Introduction and Summary
Auction design framework:
  Auction format
  Clearing price
  Compensation
  Representing constraints
Grid Code
Local security of supply and market power

## Slide 24: Compensation of in-merit unsuccessful bidders
Should we pay bidders who are in-merit in unconstrained merit order, but not selected for constraint reasons?
Less relevant under Auction format option B, only applies to inflexible units
Stakeholder response: Mixed response but support for Option 1: No compensation
Emerging thinking: Option 1
Reasons not to do so:
  Fairness: had option to bid flexibly
  Costs customers more, at least in short run
  No guarantee over longer term benefit
Options considered
Option 1: No compensation
Option 2: Lost profit (clearing price – bid price)
Option 3: Pay-as-bid

## Slide 25: Content
Introduction and Summary
Auction design framework:
  Auction format
  Clearing price
  Compensation
  Representing constraints
Grid Code
Local security of supply and market power

## Slide 26: Representation of constraints: nested zones
In the LSS consultation we discussed how the constraints would be represented in the model, and listed three options:
Option 1: A separate capacity requirement for each constrained capacity area, measured in MW (Z= X+ Y)
Option 2: A separate capacity requirement for each constrained capacity area, measured in number of capacity market units (albeit the overall target for the whole market would still be measured in MW).
Option 3: Nested capacity areas (with capacity requirements specified in MW, Z> X+Y)
Northern Ireland X MW
Dublin area Y MW
All-island Z MW
Nested areas
Option 3 the logical option- consistent with the way constraints represented in other markets, but awaiting TSO confirmation of ability to represent constraints this way

## Slide 27: Content
Introduction and Summary
Auction design framework:
  Auction format
  Clearing Price
  Compensation
  Representing constraints
Grid Code
Local security of supply and market power

## Slide 28: Grid Code
Grid Codes in Northern Ireland and Ireland require:
  Generators (greater than 50MW) to give the respective TSOs 3 years’ notice of their intention to close capacity.
  For generators below 50MW the requirement is for 2 years notice
Implications:
  Transitional auctions: A generator which loses a transitional auction held in 2017 for Capacity Delivery Years 2017/18 or 2018/19 would be prohibited from closing in those years by its Grid Code. Is this appropriate?
  T-4 auctions: Alternatively, should Grid Code requirement be extended from 3 years notice, to say 3 years 6 months or 4 years 6 months to align with T-4 auction timings?

## Slide 29: Grid Code: Stakeholder Responses
Cannot rely on Grid Code 3 year notice
  Not financeable if fail to win in CRM auction
  Legal concerns
  RAs duty to have regard for licencee’s financeability – needs remunerated
  CRM encourages exit but Grid code prevent timely exit
  TSOs concerned if Grid Code is not complied with
Some respondents proposed to align with T-1 auction flexibility and change to 3 months, others propose 1 year.

## Slide 30: Grid Code: Emerging thinking
Recognise statutory duties
But may be ancillary service reasons why a plant is needed for local security of supply
Need to consider all requirements, hence derogation not automatic to allow fall-back ancillary service arrangements to be put in place
Where no local security of supply issues, request for derogation would be sympathetically received

## Slide 31: Content
Introduction and Summary
Auction design framework:
  Auction format
  Clearing Price
  Compensation
  Representing constraints
Grid Code
Local security of supply and market power

## Slide 32: Additional market power issues
Existing plant only
Where a generator has local market power due to the constraints, it has an increased ability to bid up to the Existing Capacity Price Cap (formerly Uniform Price-taker Offer Cap).
Should we place restrictions on the bids of any plant required for local security of supply reasons, such as:
  Bid at its individual Net Going Forward Cost; or
  Bid at the Existing Capacity Price Cap adjusted for any specific ancillary service payment it may receive.
  Under further consideration
New plant only
Should we be concerned at potential to earn 10-year pay-as-bid RO in a constrained location with little competition? And are any further limits appropriate? 1 year RO only for any pay-as-bid capacity providers (i.e. out-of-merit in unconstrained merit order). Significant potential for small new build on existing sites, with market power
Extensive market power control framework put in place in CRM Decision 3, but without reference to transmission constraints
All plant
Should we publish zonal capacity requirements/demand curve in interests of transparency, or does this exacerbate market power concerns? Yes, in interests of transparency. Little to be gained in not publishing. Other remedies for market power